## Slide 1
Design and Analysis of a Complementary
Inverter-Based Low Noise Amplifier
for GPS L1 Band (1.575 GHz) in 100 nm CMOS Technology
Prakhar Singh · Sudeep Sharma · Pratik Shekhar
School of Electrical Engineering, Manipal Institute of Technology (MIT)
Manipal Academy of Higher Education (MAHE), Manipal, Udupi, Karnataka 576104
IEEE-Style Technical Presentation

## Slide 2
I. INTRODUCTION
SECTION I
GPS L1 carrier at 1.575 GHz — received signal as low as −130 dBm at antenna
LNA is the dominant noise contributor in the receive chain
LNA must simultaneously satisfy three competing requirements:
  Good impedance matching to 50 Ω antenna system
  Sufficient gain to suppress downstream stage noise (Friis chain)
  Adequate linearity to handle out-of-band interferers
Classical solution: Inductive Source Degeneration (ISD) topology
ISD enables simultaneous noise and power matching via noiseless passive inductors
This work: deliberate pedagogical constraint — NO LC matching networks
Goal: expose raw, intrinsic performance limits of a CMOS inverter in 50 Ω RF system
Key Insight: Reactive matching networks are not optional — they are fundamental to meeting GPS L1 specs.
Prakhar Singh, Sudeep Sharma, Pratik Shekhar | MIT MAHE | 2

## Slide 3
II. CIRCUIT DESIGN & METHODOLOGY — A. Topology Overview
SECTION II-A
Amplifier core: PMOS transistor M3 + NMOS transistors M1 & M2
Configured as a complementary CMOS inverter
Input RF signal AC-coupled via C1 = 10 pF to common gate of M1 and M3
Drain currents add constructively at output node
Combined small-signal transconductance: Gm = gmN + gmP
Output coupling: C2 = 1 µF passes RF to 50 Ω load (R1), blocks DC
No LC matching elements: no Ls, no Lg, no cascode
SCHEMATIC OVERVIEW
VDD (1.5 V)
|
[M3] PMOS
W=10µm L=100nm
|
[M1] NMOS
W=100µm L=100nm
| ←── OUT node
[M2] NMOS (bias)
W=100µm L=100nm
|
GND
C1(10pF) → Vin | C2(1µF) → RL(50Ω)
Prakhar Singh, Sudeep Sharma, Pratik Shekhar | MIT MAHE | 3

## Slide 4
II. CIRCUIT DESIGN & METHODOLOGY — B. Active Feedback Biasing
SECTION II-B
Challenge: Without feedback, output voltage of CMOS inverter is highly PVT-sensitive
Solution: Ideal op-amp U1 configured as feedback comparator
  U1 non-inverting input → V3 = 0.75 V (= VDD/2)
  U1 inverting input monitors V(out)
  Op-amp output drives gate of M2 (variable current source)
Closed loop forces V(out) = VDD/2 at DC — maximises symmetric voltage swing
DC Operating Point Results (.op simulation)
V(out)
0.750 V
Id (M1=M2=M3)
0.5625 mA
IDD (total)
0.617 mA
Power
0.925 mW
Key Insight: Active op-amp bias achieves PVT-robust DC centering at VDD/2 — maximises linear dynamic range.
Prakhar Singh, Sudeep Sharma, Pratik Shekhar | MIT MAHE | 4

## Slide 5
II. CIRCUIT DESIGN & METHODOLOGY — C. Transistor Sizing Rationale
SECTION II-C
NMOS M1 & M2: W = 100 µm, L = 100 nm → W/L = 1000
  Maximises NMOS transconductance (KP_N = 200 µA/V²)
PMOS M3: W = 10 µm, L = 100 nm → W/L = 100
  Exploits 2:1 KP_N / KP_P ratio to equalise current-drive — prerequisite for DC centering
Estimated Transconductances @ Bias
gm1 = √(2 · KP_N · (W/L)₁ · ID) ≈ 15 mA/V
gm3 = √(2 · KP_P · (W/L)₃ · ID) ≈ 3.35 mA/V
Effective Gm at 1.575 GHz ≈ 12.9 mA/V (reduced by parasitic capacitances)
Key Insight: Parasitic CGSO, CGDO = 2×10⁻¹⁰ F/m and CJ = 4×10⁻⁴ F/m² reduce effective Gm from DC value to ~12.9 mA/V at RF.
Prakhar Singh, Sudeep Sharma, Pratik Shekhar | MIT MAHE | 5

## Slide 6
III. SIMULATION RESULTS & ANALYSIS — A. Forward Gain (S21)
SECTION III-A
AC simulation result: S21 = −3.8 dB at 1.575 GHz
This is NOT a design error — it is a mathematically inevitable outcome
  Root cause: high-impedance current source (rds1 ∥ rds3 ≫ 50 Ω) driving 50 Ω directly
  No intervening LC impedance transformer → severe power mismatch
Phase response: −105° at 1 MHz → −182° at 1 GHz (inverting common-source + RC pole lag)
Voltage Gain:
|Av| = Gm · RL = 12.9×10⁻³ × 50 = 0.645 V/V = −3.8 dB
S21 (Gain)
−3.8 dB
Key Insight: Without LC matching, the CMOS inverter cannot deliver power efficiently to 50 Ω — fundamental physics.
Prakhar Singh, Sudeep Sharma, Pratik Shekhar | MIT MAHE | 6

## Slide 7
III. SIMULATION RESULTS & ANALYSIS — B. Input & Output Reflection (S11, S22)
SECTION III-B
S11 — Input Reflection
Result: S11 ≈ 0 dB (flat across band)
Total reflection at input port
Gate impedance is purely capacitive
  CGS + CGDO + CGSO → several kΩ at 1.575 GHz
No gate inductor Lg + Ls → cannot synthesise real 50 Ω
|Γin| → 1 (complete mismatch)
S22 — Output Reflection
Result: S22 peaks near 580 mdB at ~30 MHz
  Caused by frequency-dependent op-amp loop phase response
S22 → 0 dB at higher RF frequencies
  Active bias loop opens → passive drain impedance dominates
No output matching network → unmatched high-impedance output
Prakhar Singh, Sudeep Sharma, Pratik Shekhar | MIT MAHE | 7

## Slide 8
III. SIMULATION RESULTS & ANALYSIS — C. Reverse Isolation (S12)
SECTION III-C
Simulated reverse isolation: S12 ≈ −225 dB at 1.575 GHz
This is the simulator's numerical floor — not a physical result
  Only reverse transmission path in schematic: gate-drain overlap capacitance
  CGDO ≈ 2×10⁻¹⁴ F (for W = 100 µm)
  Feedback admittance at 1.575 GHz: Yfb = jωCGDO ≈ j0.2 µS (extremely small)
Physical implementation expectation: S12 = −30 to −50 dB
  Degraded by substrate coupling and package parasitics in real layout
S12 (Simulated)
−225 dB
S12 (Physical Est.)
−30 to −50 dB
Prakhar Singh, Sudeep Sharma, Pratik Shekhar | MIT MAHE | 8

## Slide 9
III. SIMULATION RESULTS & ANALYSIS — D. Noise Figure (NF)
SECTION III-D
NF simulation expression: 10·log₁₀(V(inoise)² / (4kTRs)) — k=1.38×10⁻²³, T=290K, Rs=50Ω
NF at 1 MHz: ~23.5 dB → rolls off to ~11.5 dB in 100 MHz–1 GHz range
  Root cause 1: Thermal channel noise from M1 & M3 (S_id = 4kTγgm)
  Root cause 2: Absence of source-degeneration inductor Ls
  Ls provides real input impedance without contributing noise
  In ISD LNA: simultaneously satisfies power match (|Γin|=0) and noise match (Ys=Yopt)
  Without Ls: power and noise match conditions are irreconcilably separated
Friis Noise Formula: NF = NFmin + (Rn / Gs) · |Ys − Yopt|²
NF @ 1.575 GHz
11.5 dB
Prakhar Singh, Sudeep Sharma, Pratik Shekhar | MIT MAHE | 9

## Slide 10
III. SIMULATION RESULTS & ANALYSIS — E. Transient Response
SECTION III-E
Transient simulation: 1.575 GHz sinusoidal input at 10 mV amplitude, 0–10 ns window
Input node V(n002) — green trace: swings 740 mV to 760 mV → 20 mVpp
Output V(out) — blue trace: swings ~748 mV to ~752 mV → 4 mVpp
Voltage gain: |Av| ≈ 4/20 = 0.2 V/V → confirms −3.8 dB gain
Output is 180° phase-inverted relative to input (common-source inverter)
DC bias of 750 mV maintained perfectly throughout — confirms stable bias loop
Transient Summary
Vin (peak-peak)
20 mVpp
Vout (peak-peak)
4 mVpp
Phase Shift
180° (inv.)
DC Bias
750 mV ✓
Prakhar Singh, Sudeep Sharma, Pratik Shekhar | MIT MAHE | 10

## Slide 11
IV. PERFORMANCE COMPARISON
SECTION IV
This Work (Constrained) vs. Reference Cascode LNA with Full LC Matching
Parameter | This Work (Constrained) | Reference Cascode LNA
Technology | 100 nm CMOS | 100 nm CMOS
VDD | 1.5 V | 1.5 V
Power (PDC) | 0.925 mW ✓ | 9–15 mW (typ.)
S21 (Gain) | −3.8 dB | +14 to +18 dB
S11 | ≈ 0 dB | < −10 dB
S22 | ≈ 0 dB | < −10 dB
S12 | ≈ −225 dB (sim. floor) | < −30 dB
Noise Figure | 11.5 dB | 1.5–3.0 dB
Matching | None (constrained) | Lg, Ls, Ld, Cd
DC Bias | Active FB (op-amp) | Passive resistive
Prakhar Singh, Sudeep Sharma, Pratik Shekhar | MIT MAHE | 11

## Slide 12
IV. PERFORMANCE COMPARISON — Analysis & Key Takeaways
SECTION IV
Power advantage: 10–16× lower power dissipation (0.925 mW vs. 9–15 mW)
  This advantage is entirely offset by all RF performance metrics
  NF of 11.5 dB vs. 1.5–3.0 dB: degrades receiver sensitivity by ~8–10 dB
  Reference NF of 1.5–3.0 dB enables the −130 dBm signal sensitivity required for GPS acquisition
  S21 deficiency of ~18–22 dB directly increases noise contribution of downstream stages
S11 ≈ 0 dB: all incident RF power is reflected — no power transfer to the LNA
Reactive matching networks provide more than impedance transformation:
  They simultaneously enable power gain, noise optimisation, and port matching
  These goals are physically unachievable without reactive elements
Key Insight: Matching networks are not optional enhancements — they are fundamental prerequisites for GPS L1 front-end specifications.
Prakhar Singh, Sudeep Sharma, Pratik Shekhar | MIT MAHE | 12

## Slide 13
V. CONCLUSION
Topology
Complementary
Inverter LNA
Technology
100 nm CMOS
Frequency
1.575 GHz
(GPS L1)
Supply
1.5 V / 0.925 mW
Active op-amp feedback bias achieves stable V(out) = 0.75 V DC operating point
S21 = −3.8 dB, S11 ≈ 0 dB, S22 ≈ 0 dB, S12 ≈ −225 dB, NF = 11.5 dB — all physically consistent with unmatched 50 Ω system
Transient simulation confirms stable 750 mV DC centering and 180° signal inversion
Comparison confirms: matching networks enable simultaneous power gain, noise opt., and port matching — unachievable without reactive elements
Future Work: On-chip spiral inductors for Ls (source degeneration) and Lg (gate matching) to achieve S11 < −10 dB and NF < 3 dB
Prakhar Singh, Sudeep Sharma, Pratik Shekhar | MIT MAHE | 13

## Slide 14
REFERENCES
REFERENCES
[1] T. H. Lee and S. S. Wong, "CMOS RF Integrated Circuits at 5 GHz and Beyond," Proc. IEEE, vol. 88, no. 10, pp. 1560–1571, Oct. 2000.
[2] D. K. Shaeffer and T. H. Lee, "A 1.5-V, 1.5-GHz CMOS Low Noise Amplifier," IEEE J. Solid-State Circuits, vol. 32, no. 5, pp. 745–759, May 1997.
[3] B. Razavi, RF Microelectronics, 2nd ed. Prentice Hall, 2011, ch. 5–6.
[4] T. H. Lee, The Design of CMOS Radio-Frequency Integrated Circuits, 2nd ed. Cambridge Univ. Press, 2004.
[5] Analog Devices, LTspice XVII User Manual, 2023.
Thank You — Questions Welcome
Prakhar Singh, Sudeep Sharma, Pratik Shekhar | MIT MAHE | 14